## Slide 1
Module4 Session1: ACE Strategy + DeepACE Paper
DeepACE Model Analysis: From Fixed Rules to Data-Driven

## Slide 2
Agenda (2.5 hours)
0:00-0:20 ACE Strategy Review: Band Allocation -> Envelope -> Channel Selection -> Stimulation
0:20-0:45 ACE Limitations: Fixed Rules, Noise Sensitivity
0:45-1:10 DeepACE Paper: Problem Definition & Methodology
1:10-1:20 Break
1:20-1:50 DeepACE Paper: Network Architecture
1:50-2:20 DeepACE Paper: Training & Experiments
2:20-2:30 Discussion

## Slide 3
Section 1-2
ACE Strategy Review & Limitations

## Slide 4
ACE Strategy Core Pipeline
Input Audio -> Preemphasis -> Framing+Windowing -> FFT -> Band Power Envelope -> N-of-M Selection -> Log Compression -> Stimulation
Key Parameters
NumberOfBands = 22 (corresponding to 22 electrodes)
Nmaxima = 8~12 (max channels selected per frame)
StimulationRate = 900~1000 Hz
THR / MCL (Threshold / Most Comfortable Level)
Core Idea
ACE divides speech spectrum into 22 bands
Each frame selects top-N channels by energy
Essence: fixed rules + energy sorting
-> Simple & predictable, but lacks adaptability

## Slide 5
ACE Output: Electrodogram
What is an Electrodogram?
X-axis = Time frames
Y-axis = Electrode channels (1~22, low to high freq)
Color/Brightness = Stimulation current level
Only Nmaxima channels active per frame
from ace_strategy import ace_strategy
q, p = ace_strategy(signal, sr, n_band=22, n_maxima=8)
q['electrodes'] # selected electrode sequence
q['current_levels'] # corresponding current levels
p['NumberOfBands'] # 22
p['Nmaxima'] # 8
Hands-on Tip
Run ACE code on synthetic speech to observe each step
Focus on: How N-of-M channel selection works -> keep only top-N energy channels

## Slide 6
ACE Limitations in Noisy Environments
Problem 1: Fixed rules don't adapt to noise
Noise occupies multiple bands -> energy ranking disrupted
Speech channels get 'squeezed out' of N-of-M selection
Problem 2: Only looks at current frame
No temporal info -> cannot exploit speech continuity
Problem 3: Fixed parameters
THR/MCL static -> don't change with input
Nmaxima fixed -> different scenes may need different counts
Core Insight
Traditional ACE uses fixed rules for all cases
DeepACE core idea: learn these rules via data-driven approach
Key comparison:
ACE: Fixed N-of-M -> hand-crafted rules
DL: Learned mask -> adaptive selection

## Slide 7
Hands-on: Clean vs Noisy Speech ACE Output
noise = np.random.randn(len(signal)) * 0.3
snr_db = 5
speech_power = np.mean(signal ** 2)
noise_power = np.mean(noise ** 2)
snr_linear = 10 ** (snr_db / 10)
noise_scaled = noise * np.sqrt(
speech_power / (noise_power * snr_linear))
noisy_signal = signal + noise_scaled
q_clean, _ = ace_strategy(signal, sr)
q_noisy, _ = ace_strategy(noisy_signal, sr)
Observation Points
How does noise change channel selection?
What is the channel selection difference ratio?
Which channels are most affected by noise?
Expected Results:
Noise occupies high-frequency channels
Speech-related channels get suppressed
Reflection
In noisy environments, CI users' speech understanding drops significantly. Traditional ACE's N-of-M cannot distinguish speech from noise - this is exactly what DeepACE aims to solve.

## Slide 8
Section 3-4
DeepACE Paper: Problem Definition & Methodology

## Slide 9
Paper Reading Methodology
Four-Pass Reading Method
Pass 1: Title + Abstract (5min)
What problem? Input/Output? One-sentence innovation?
Pass 2: Introduction (10min)
Limitations of existing methods? Why DL? Contributions?
Pass 3: Method (20min)
Architecture? What does each layer do? Loss function?
Pass 4: Experiments (10min)
Data construction? Metrics? Ablation study?
Reading Guide Checklist
What problem does DeepACE solve?
What is the input? What is the output?
Core innovation in one sentence?
What are ACE's specific limitations?
Why use DL for this problem?
What does Encoder do? Which ACE step?
What is Mask Generator similar to (Module 3)?
Why 22 output channels?
What loss function? Why this choice?
How is training data constructed?
Results vs traditional ACE? Where is the advantage largest?

## Slide 10
Section 5-6
DeepACE Paper: Network Architecture

## Slide 11
DeepACE Architecture Overview
Input: Noisy speech WAV (batch, 1, T_samples)
|
v
+--------------+
| Encoder | Conv1d(1->N, kernel=L, stride=L/2)
| | Output: (batch, N, T')
+--------------+
|
v
+--------------+
| Rectifier | Learnable activation (pos/neg decomposition)
| | Output: (batch, N, T')
+--------------+
|
v
+---------------------------+
| Mask Generator | R Stacks x X ConvBlocks
| Mask output: (batch,22,T')| SE Layer + LAuReL + Skip
+---------------------------+
| feats * mask -> masked features
v
+--------------+
| Decoder | ConvTranspose1d(N->22)
+--------------+
|
v
+---------------------+
| ChannelRebalancer | Inter-channel rebalancing
+---------------------+
|
v
Hardtanh -> Output: Electrodogram (batch, 22, T')
Key Understanding
DeepACE needs no explicit FFT, framing, or band division
-> All learned implicitly by encoder convolutions
Encoder ~ Learned Time-Freq Analysis
Conv1d replaces FFT + band division
stride=L/2 ~ hop_length
Mask Generator ~ Adaptive N-of-M
Outputs 22-channel mask (0~1)
Mask value ~ channel selection probability
Decoder ~ Electrodogram Reconstruction
High-dim features -> 22 channels
ChannelRebalancer ~ Adaptive THR/MCL

## Slide 12
DeepACE vs Prior Knowledge Mapping
Each DeepACE component has a counterpart in Modules 2-3
DeepACE Component
Module 2-3 Knowledge
Innovation
Encoder (Conv1d)
Module 2 CNN
Like spectrogram extraction, but learned
Rectifier
ReLU activation
From fixed rule to learnable parameters
ConvBlock
Module 3 CRNN conv layers
SE attention + LAuReL residual
Skip Connection
Module 2 ResNet
Same skip connections as UNet
Mask (Sigmoid)
Module 3 attention
22-channel mask = 22 electrodes
ChannelRebalancer
--
CI-specific: balance inter-channel stimulation

## Slide 13
Section 7-8
DeepACE Paper: Training & Experiments

## Slide 14
Training Data Construction
Paired Data
Clean speech + Noise = Noisy speech (mixture)
Input: mixture WAV (16kHz)
Clean speech -> ACE -> Electrodogram (target)
Target: .mat (T, 22) -> transpose -> (22, T)
Key Design
Input = noisy speech
Target = electrodogram from clean speech via ACE
Comparison
Speech Enh.
DeepACE
Input
Noisy speech
Noisy speech
Output
Clean spectrogram
Clean electrodogram
Domain
Time-frequency
CI stimulation
Loss
Spectrogram MSE
Electrodogram MSE
Connection to Module 5
DeepACE and speech enhancement (Module 5) share the same philosophy - both recover clean from noisy, just in different output domains.

## Slide 15
Discussion Questions
Question 1
Encoder uses Conv1d to replace FFT+band division. Advantages? Potential issues?
Question 2
Cost of obtaining paired data? Alternatives without paired data?
Question 3
What does causal=True mean in config.yaml? Why does CI need causality?
Question 4
Does DeepACE replace ACE entirely or improve upon it? Pros/cons?
Question 5
Will the model work with unseen speakers/noise?

## Slide 16
Summary & Homework
What we did today:
Reviewed ACE strategy pipeline with code verification
Observed noise impact on ACE channel selection
Understood limitations of traditional methods
Read DeepACE paper with structured methodology
Mapped DeepACE architecture to prior knowledge
Homework
Complete all questions in the reading guide
Draw DeepACE data flow diagram with tensor shapes at each step
Pre-read: DeepACE_torch/ code files
Next Session
DeepACE Code Analysis & Running - from understanding paper to running code