## Slide 1
Module5 Session1: Speech Enhancement Basics + DeepFilterNet Paper
From Noisy to Clean: Understanding the SE Problem & DeepFilterNet Architecture

## Slide 2
Agenda (2.5 hours)
0:00-0:20 SE Problem Definition: Recover clean speech from noisy input
0:20-0:45 SE Evaluation Metrics: PESQ, STOI, SI-SDR
0:45-1:10 Traditional SE Methods: Spectral Subtraction, Wiener Filter
1:10-1:20 Break
1:20-1:50 DeepFilterNet Paper: Architecture Design
1:50-2:20 DeepFilterNet Paper: Training & Experiments
2:20-2:30 Discussion: DeepFilterNet and CI/Hearing Aids

## Slide 3
Section 1-2
SE Problem Definition & Evaluation Metrics

## Slide 4
Speech Enhancement Problem Definition
Signal Model: x(t) = s(t) + n(t)
x(t) = noisy speech (observation)
s(t) = clean speech (target) n(t) = noise (interference)
SE Goal
Estimate s(t) from x(t), minimizing |s_hat(t) - s(t)|
In CI Context
x(t) = CI microphone picks up noisy speech
s(t) = ideal clean speech CI user should receive
SE is frontend processing, ACE is backend encoding
Processing Pipeline
Noisy Audio -> [SE Enhancement] -> Enhanced Audio -> [ACE Encoding] -> Electrodes
Module 5 covers the SE enhancement step
Module 4 covered the ACE encoding step
Together they form a complete CI frontend

## Slide 5
Hands-on: Generating Noisy Speech at Different SNRs
# Generate clean speech (harmonics)
f0 = 150
clean = sum((0.5/h) * np.sin(2*np.pi*f0*h*t) for h in range(1, 10))
clean = clean / np.max(np.abs(clean)) * 0.8
# Generate noise
noise = np.random.randn(len(t)) * 0.3
# Mix at target SNR
def mix_at_snr(clean, noise, snr_db):
clean_power = np.mean(clean ** 2)
noise_power = np.mean(noise ** 2)
snr_linear = 10 ** (snr_db / 10)
noise_scaled = noise * np.sqrt(
clean_power / (noise_power * snr_linear))
return clean + noise_scaled
noisy_0db = mix_at_snr(clean, noise, 0)
noisy_5db = mix_at_snr(clean, noise, 5)
noisy_10db = mix_at_snr(clean, noise, 10)
SNR Explained
SNR = Signal-to-Noise Ratio
Higher SNR = less noise = easier to enhance
Lower SNR = more noise = harder to enhance
Typical CI environments:
Quiet room: SNR ~ 20-30 dB
Office: SNR ~ 5-15 dB
Restaurant: SNR ~ -5 to 5 dB
Street: SNR ~ 0-10 dB

## Slide 6
Traditional SE Methods
Spectral Subtraction
|S_hat(f)|^2 = |X(f)|^2 - |N_hat(f)|^2
Simple: subtract noise spectrum from noisy spectrum
Problem: creates 'musical noise' artifacts
Wiener Filter
H(f) = P_ss(f) / (P_ss(f) + P_nn(f))
Optimal linear filter minimizing MSE
Requires estimating speech and noise power spectra
Limitation of both methods:
Fixed rules based on statistical assumptions
Cannot adapt to complex, non-stationary noise
-> This motivates deep learning approaches
# Spectral Subtraction
noise_power = np.abs(noise_fft) ** 2
estimated = np.abs(noisy_fft)**2 - noise_power
estimated = np.maximum(estimated, 0) # no negatives!
enhanced = np.sqrt(estimated) * np.exp(1j * np.angle(noisy_fft))
# Wiener Filter
wiener_gain = clean_power / (clean_power + noise_power + 1e-8)
enhanced_wiener = wiener_gain * noisy_fft
# Both return to time domain via IFFT
enhanced_signal = np.real(ifft(enhanced))

## Slide 7
SE Evaluation Metrics: PESQ, STOI, SI-SDR
Three core objective metrics for speech enhancement
Metric
What it Measures
Range
CI Relevance
PESQ
Perceptual speech quality
-0.5 ~ 4.5
CI user perceived quality
STOI
Short-time intelligibility
0 ~ 1
Can CI user understand? CRITICAL!
SI-SDR
Signal distortion ratio
-inf ~ +inf dB
Overall enhancement quality
Key Insight
CI users care most about INTELLIGIBILITY (STOI), not just quality (PESQ)
Speech enhancement must help CI users UNDERSTAND, not just sound good
Why improving SI-SDR alone may not improve STOI: SI-SDR measures signal-level distortion, ignores perceptual aspects

## Slide 8
Section 3-4
DeepFilterNet Paper: Architecture & Training

## Slide 9
DeepFilterNet Paper Reading Guide
Four-Pass Reading Method
Pass 1: Title + Abstract (5min)
What is Deep Filtering? How does it differ from traditional filtering?
Why ERB domain instead of Mel?
Pass 2: Introduction (10min)
Limitations of traditional SE methods?
Why is DL better for SE?
Pass 3: Method (20min)
Why two stages (Enhancement + Deep Filtering)?
ERB domain vs STFT domain?
Deep Filtering formula?
Pass 4: Experiments (10min)
Training data construction?
Evaluation datasets and metrics?
Paper Structure
Schrter et al. 'DeepFilterNet: A Low Complexity Speech Enhancement Framework for Real-Time On-Device Processing' arXiv 2023
Core Innovation: Two-stage design
Stage 1: Enhancement (ERB mask-based)
Stage 2: Deep Filtering (learned FIR filter)
Key Design Choices:
ERB domain (not Mel) -> closer to auditory perception
GroupedGRU -> reduces parameters while maintaining capacity
alpha parameter -> controls DF stage contribution
Real-time capable (~5ms latency)

## Slide 10
DeepFilterNet Two-Stage Architecture
Stage 1: Enhancement (mask-based)
Input: Noisy spectrogram (STFT)
|
+-- ERB feature extraction -> 32 ERB bands
+-- Encoder (2D Conv) -> GroupedGRU -> ErbDecoder (U-Net)
|
Output: ERB domain mask [0, 1]
Apply: enhanced = spec * mask (pre-enhancement)
Stage 2: Deep Filtering (learned FIR)
Input: Pre-enhanced spectrogram
|
+-- DF branch in Encoder -> DfDecoder (GroupedGRU)
| -> DF coefficients (order x bins)
| -> alpha (mixing weight)
|
Operation on low-freq bins:
Y[f] = sum_k C[k,f] * X[f-k] (complex conv)
Mix: output = alpha * DF_result + (1-alpha) * mask_result
|
Output: Final enhanced spectrogram
Full pipeline:
Noisy WAV -> STFT -> Stage1 -> Stage2 -> iSTFT -> Clean WAV
Why Two Stages?
Stage 1 (Enhancement)
Mask-based: simple, fast, good baseline
ERB domain: coarse frequency processing
Stage 2 (Deep Filtering)
Learned FIR filter for fine refinement
Only on low-frequency bins (where speech energy is)
alpha controls how much DF contributes
ERB vs Mel
Mel: based on pure tone perception
ERB: based on noise band perception
ERB is closer to actual auditory resolution
CI electrode mapping follows ERB-like nonlinear mapping

## Slide 11
DeepFilterNet vs Prior Knowledge
Each DeepFilterNet component has a counterpart in prior modules
DFN Component
Prior Knowledge (Module 2-4)
Innovation
ERB feature extraction
Module 3 Mel spectrogram
ERB scale: closer to auditory perception
Enhancement (mask)
Module 2 spectrogram classification
Output mask instead of class labels
Deep Filtering
Traditional FIR filter
Network learns filter coefficients
GroupedGRU
Module 3 GRU
Split GRU into groups, fewer parameters
U-Net decoder
Module 2 CNN + ResNet
Skip connections for multi-scale features
alpha parameter
--
Adaptive mixing: model chooses when to use DF

## Slide 12
ERB vs Mel Scale: Connection to CI
Mel Scale
Based on pure tone perception experiments
Commonly used in ASR and sound classification
Standard in modules 2-3
ERB Scale
Based on noise band perception experiments
Closer to actual human auditory frequency resolution
DeepFilterNet's choice for SE
CI Connection
Modern CI: 22 electrodes ~ 22 ERB bands
CI electrode frequency allocation follows ERB-like nonlinear mapping
DeepFilterNet: 32 ERB bands (more refined, CI-compatible)
16 ERB bands ~ early CI processors
22 ERB bands ~ matches CI electrode count
32 ERB bands ~ DeepFilterNet default
48 ERB bands ~ close to normal hearing
Why This Matters for CI
ERB scale has a MORE DIRECT relationship to CI than Mel scale. CI electrode frequency allocation inherently follows ERB-like nonlinear mapping. Understanding ERB helps connect SE research to CI applications.

## Slide 13
Discussion Questions
Question 1
Traditional methods (spectral subtraction, Wiener) vs DL: pros and cons of each paradigm?
Question 2
Evaluating SE for CI users: PESQ or STOI? Why?
Question 3
Why does Deep Filtering only operate on low frequencies? How does this relate to speech signal properties?
Question 4
If DeepFilterNet is placed before ACE (enhance-then-encode), how would it affect channel selection?
Question 5
DeepFilterNet is designed for real-time (~5ms latency). Why is this critical for CI/hearing aids?

## Slide 14
Summary & Homework
What we did today:
Understood SE signal model and problem definition
Implemented traditional methods and observed limitations
Deep-dived into PESQ, STOI, SI-SDR metrics
Read DeepFilterNet paper with structured methodology
Connected ERB domain to CI electrode mapping
Homework
Complete all questions in the paper reading guide
Draw DeepFilterNet complete data flow diagram
Pre-read: DeepFilterNet/df/ code files
Next Session
DeepFilterNet Code Analysis & Running - from understanding paper to running code