## Slide 1
Module5 Session3 (Optional): DeepFilterNet + CI Integration
Experiments: ERB Band Modifications, Enhance-then-Encode Pipeline, Latency Analysis

## Slide 2
Agenda (2.5 hours)
0:00-0:15 Review + Questions
0:15-0:45 Exp 1: Modify ERB band count, observe frequency resolution impact
0:45-1:15 Exp 2: DeepFilterNet output -> ACE strategy (Enhance-then-Encode pipeline)
1:15-1:25 Break
1:25-1:55 Exp 3: SNR sweep evaluation of enhancement quality
1:55-2:20 Latency analysis: Can DeepFilterNet meet CI real-time requirements?
2:20-2:30 Summary: Gap from general SE to CI-specific SE

## Slide 3
Section 1
Experiment 1: ERB Band Count Modifications

## Slide 4
ERB Frequency Band Analysis
Hypothesis
Changing ERB band count affects frequency resolution.
Fewer bands = coarser representation but possibly more noise-robust.
This tradeoff mirrors CI electrode count decisions.
# Compare ERB filterbanks
for n_erbs in [16, 32, 48]:
fb = erb_filterbank(n_erbs, sr=48000, n_fft=960)
# Visualize filterbank shape
# Wider bands = more noise averaging
# Narrower bands = finer frequency detail
# In config.py: NB_ERB parameter
# Default: 32 ERB bands
# Modify to test: 16, 22, 32, 48
CI Connection
16 ERB bands: similar to early CI processors (coarse frequency resolution)
22 ERB bands: matches modern CI electrode count (direct mapping possible)
32 ERB bands: DeepFilterNet default (good balance, CI-compatible)
48 ERB bands: closer to normal hearing resolution

## Slide 5
Section 2
Experiment 2: Enhance-then-Encode Pipeline

## Slide 6
DeepFilterNet -> ACE Pipeline
# Pipeline Design
# Noisy -> DeepFilterNet -> Enhanced -> ACE -> Electrodogram
# Step 1: Enhance with DeepFilterNet (48kHz)
enhanced = enhance(model, df_state, noisy_audio)
# Step 2: Resample to CI rate (48kHz -> 16kHz)
enhanced_16k = torchaudio.functional.resample(
enhanced, 48000, 16000)
# Step 3: Run ACE strategy
q, p = ace_strategy(enhanced_16k.numpy(),
sr=16000, n_band=22, n_maxima=8)
# Baseline comparison:
# Noisy -> ACE -> Electrodogram (no enhancement)
Pipeline Comparison
With Enhancement:
Noisy -> DFN -> Enhanced -> ACE -> Electrodes
Without Enhancement (baseline):
Noisy -> ACE -> Electrodes
Key Metric:
Channel selection difference ratio
Does enhancement improve ACE channel selection?
Sample Rate Challenge
DeepFilterNet works at 48kHz, ACE uses 16kHz
Must resample between stages (potential information loss)
Alternative: train a 16kHz version of DeepFilterNet specifically for CI
This is an active research direction in CI speech processing

## Slide 7
Experiment 3: SNR Sweep Evaluation
# Test across SNR range
snr_levels = [-10, -5, 0, 5, 10, 15, 20]
results = []
for snr in snr_levels:
noisy = mix_at_snr(clean, noise, snr)
enhanced = enhance(model, df_state, noisy)
si_sdr_in = compute_si_sdr(noisy, clean)
si_sdr_out = compute_si_sdr(enhanced, clean)
improvement = si_sdr_out - si_sdr_in
results.append((snr, si_sdr_in, si_sdr_out, improvement))
Hypothesis
Enhancement effect degrades at very low SNR
There exists an SNR threshold below which enhancement has minimal benefit
Expected Curves
Input SI-SDR: linearly increases with SNR
Output SI-SDR: also increases, but with diminishing returns
Improvement: peaks at moderate SNR, drops at extremes
What to Look For
SNR = -10dB: Enhancement barely helps (noise too dominant)
SNR = 0~5dB: Enhancement provides most benefit (typical CI challenging environments)
SNR = 15~20dB: Less improvement needed (already relatively clean)
The sweet spot for SE benefit overlaps with the hardest CI listening situations!

## Slide 8
Latency Analysis: Real-Time CI Requirements
Application
Max Latency
DFN Algorithmic Latency
Hearing aids
5-10 ms
~5 ms
CI processors
5-10 ms
~5 ms
Phone calls
~150 ms
~5 ms
Video calls
~200 ms
~5 ms
DFN Latency Calculation
hop_size / sr = 480 / 48000 = 10ms
With 50% overlap, effective latency ~ 5ms
CI Deployment Challenges:
1. Compute budget: CI ~ 1/10 of smartphone power
2. Power: must run 12+ hours on battery
3. Model size: ~1.5M parameters (too large?)
4. Fixed-point: CI HW may not support float32
Why Latency Matters
Lip-sync: if audio is delayed > 30ms, visual-audio mismatch is noticeable
Own voice: delayed feedback makes speaking difficult
Conversational flow: > 200ms delay disrupts natural turn-taking
For CI/hearing aids: algorithmic + hardware latency must stay < 10ms
DFN's ~5ms is promising but real hardware adds more latency

## Slide 9
Gap Analysis: General SE vs CI-Specific SE
Aspect
General SE
CI-Specific SE
Optimization target
PESQ (quality)
STOI (intelligibility)
Frequency range
Full bandwidth
CI-relevant frequencies only
Noise types
Any noise
CI-typical environments (restaurant, street)
Output
Single enhanced audio
Must feed into CI encoder (ACE)
Latency
Nice to have
MUST be < 10ms
Evaluation
Objective metrics
CI user subjective tests (gold standard)

## Slide 10
Research Directions: Bridging the Gap
1. CI-aware Loss Function
Include ACE channel selection quality in training loss
2. Joint Optimization
End-to-end training of SE + CI encoder
3. Per-Electrode Enhancement
Different enhancement per CI channel
4. Noise Type Adaptation
Focus on noise types most problematic for CI users
5. Model Compression
Quantization, pruning for CI hardware deployment
6. CI User Subjective Evaluation
Gold standard: let CI users directly evaluate

## Slide 11
Summary
What we did today:
Analyzed ERB band count and its CI connection
Built Enhance-then-Encode pipeline (DFN + ACE)
Evaluated enhancement across SNR range
Analyzed real-time requirements for CI deployment
Discussed gap between general SE and CI-specific SE
Homework
Basic: Run DFN inference on 3 files at different SNRs, compute metrics
Advanced: Build complete enhance->ACE pipeline, compare channel selection with/without enhancement
Module 5 Core Takeaway
DeepFilterNet provides a practical, real-time capable SE solution. Connecting it to CI processing reveals both opportunities and challenges for CI-specific SE research.